## Slide 1: Evolutionary Optimization Algorithms
Raymond Huang | Armaan Mehta | Holiday Han
Yunruih2 | Armaanm3 | Ziyinh2
ME 447 Project 3

## Slide 2: Table of Contents
Objective
Snake force implementations
CMA-ES implementation
Optimization of the pure wiggling case (CMA)
Optimization of the pure twitching case (CMA)
Optimization of the combined case (CMA)
Comparison and Conclusion

## Slide 3: Objective
After implemented the computational soft mechanics code and construct a near-realistic model of a slithering snake and use CMA to find gait parameters that maximizes the forward speed, under given conditions in project 2, we want to have a more real-life soft mechanics model based on the snake we have already had.
This project is created for studying the effect of wiggling in snake gaits. In real life situations, when a snake moves, it does not only slither due to movements created by muscle torque, but it also extends and shrinks, what we defined as wiggle. We want to optimize the gait with CMA to find which combination of wiggling and slithering maximizes the forward speed? That is what we are studying in this project.

## Slide 4: Snake force implementation - stretching
We defined the stretching force in our project as shown on the right
Total force has a magnitude given by its normalized length based on the Beta spline coefficients
The snake choose between crawling and slithering, percent_crawling means how much percent of force is used to generate stretching force that results in wiggling.
Stretching is an internal force, therefore perform in place addition for the tail nodes as they are pulled forward, and in place subtraction for head nodes as they pulled backwards by reaction forces.

## Slide 5: Snake force implementation - slithering
We defined the twisting torque in our project as shown on the right
As the snake contract its muscle, unbalanced force on the sides create force couples, thus generating torques.
We assume the forces are equal and opposite direction on the two side of the snake, therefore there is a moment arm = diameter of the snake
As this is an internal torque, we need in place addition and subtraction with the same reason we do for the stretching force.

## Slide 6: CMA-ES Parallel implementation
We implemented the CMA evolution strategy as described in the paper and project 1
Termination criteria were implemented which improves the speed of the algorithm as it stops when the algorithm has reached an optimum solution or if an indicator exists hinting to the algorithm not converging at all saving computational time and cost
We implemented a function called parallel_sort() which utilized all cores and sorted the population based on the fitness function in a more efficient manner
  Using multiprocessing, we were able to parallelize the process of finding the fitness values across all cores in each population member before combining that information to sort the population
  Increased the speed of CMA-ES for our implementation ~5.5x on a 6-core laptop allowing us to increase popsize and sigma
  This meant that the optimized solution had a far greater likelihood of being the most optimum solution that existed within our boundaries defined in the fitness function

## Slide 7: Defining the fitness function
The fitness function returned the speed of the snake across all axes in m/s
A penalty system was applied if the b-spline coefficients or the wavelength exceeded or went below a value as shown beside
  This allowed us to constrain the parameters in an efficient manner
  A penalty system was deemed better than returning zero as the fitness as we would have to increase pop_size if we chose to do that
The CMA-ES_Parr function optimized for the largest fitness therefore maximum speed

## Slide 8: Optimization of the pure wiggling case (CMA)
Initial Sigma = 30, Population size = 50, Max_Generations = 250, % Crawling = 100
  Solution: b_coeff = [ 0, -150.19929554, 499.68705001, 499.708699, 489.26091413, 0 ], wave_length = 285.0082 cm
  Fitness: 0.163 m/s
  Terminated in 95 Iterations (NoEffectCoor)

## Slide 9: Optimum gait of the pure wiggling case (Results)

## Slide 10: Optimization of the pure twitching case (CMA)
Initial Sigma = 30, Population size = 50, Max_Generations = 250, % Crawling = 0
  Solution: b_coeff = [ 0, 135.65041025, 211.66918051, 499.5960613, 498.99765331, 0 ], wave_length = 147.94281119 cm
  Fitness: .223 m/s
  Terminated in 87 Iterations (NoEffectCoor)

## Slide 11: Optimum gait of the pure twitching case (Results)

## Slide 12: Optimization of the combined twitching and wiggling case (CMA)
Initial Sigma = 30, Population size = 80, Max_Generations = 250
  Solution: b_coeff = [ 0, 1.17293510e+02, 2.86312534e+02, 4.30534094e+02, 4.85093523e+02, 0 ], wave_length = 1.49971895e+02 cm
  Fitness: 0.219 m/s
  Terminated in 28 Iterations (ConditionCov)

## Slide 13: Optimum gait of the combined twitching and wiggling case (Results)

## Slide 14: Comparison and Conclusion

## Slide 15: The End. Thank you for listening